## Slide 1
Grotrian-Steinweg-Str. 1c
D-38112 Braunschweig
( +49 531 23000-0
6 +49 531 23000-10
: www.kito.de
* info@kito.de
Your specialist in Explosion Protection

## Slide 2
Applications of KITO® devices

## Slide 3: Protection of tanks above ground – endurance burning proof performance
Filling line:
Wet Detonation Arrester, uni-directional KITO® FL/INO-…-IIB3 (G 14.1 N)
In-and outbreathing:
Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/MC-IIA-…-… (E 16.9 N)
Gas balance line:
Detonation Arrester, uni-directional, short time burning proof KITO® FDN-Det4-IIA-…-1,2 (G 18.1 N) with in line pressure and vacuum relief valve KITO ® VD/TG-… (F 31 N)
Protection for flammable liquids :
•For liquids with flaspoints < 55 °C (TRBS 2154 / TRbF 20)
•For liquids with flashpoints < 60 °C / 140 °F (API 2000 / ISO 28300)

## Slide 4: Protection of tanks above ground – explosion-proof without endurance burning proof
In – and outbreathing:
Deflagration proof Pressure and Vacuum Relief Valve
KITO® VD/AE-…-IIB3 (E 20 N)
Emergency venting:
Pressure Relief Valve
KITO® EV/o-… (C 10.1.N)
(Fire case)
Protection of flammable liquids :
•For liquids with flashpoint
< 60 °C/-140 °F
(API 2000 / ISO 28300)

## Slide 5: Protection of tanks above ground for none flammable liquids
Venting and breathing:
Pressure and vacuum relief valve KITO® VD/oG-…
(E 21 N)
Emergency venting: Pressure relief valve
KITO® EV/o-… (C 10.1.N) (fire case)

## Slide 6: Example of protection of tanks above ground – KITO® flame arrester devices

## Slide 7
Suction and filling line :
Uni-directional end-of-line liquid detonation flame arrester KITO® FL/IN-...-IIB3 (G 14 N)
Uni-directional in-line detonation flame arrester, short-time burning proof KITO® FD4-Det4-IIB1-…-1,2 (G 19.3 N)
Armatures for ventilation / exhaust air / gas compensation / N2- overlaying:
Deflagration proof vacuum relief valve KITO® VS/o-… (D 12 N)
Bi-directional in-line detonation flame arrester, short-time burning proof KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)
Inline devices :
In-line pressure and vacuum relief valve KITO® VD/o3-… (F 18 N)
In-line pressure and vacuum relief valve KITO® VD/T-… (F 33 N)
In-line pressure and vacuum relief valve KITO® VD/T3-… (F 37 N)
In-line pressure or vacuum relief valve KITO® VL/TA-… (F 50 N)

## Slide 8: Protection of underground tanks

## Slide 9
Filling pipe:
Uni-directional end-of-line liquid detonation flame arrester KITO® FL/INO-...-IIB3 (G 14.1 N)
Breather for filling pipe:
Bi-directional in-line detonation flame arrester KITO® FS-Det4-IIA-…-1,2 (G 30 N)
Suction pipe:
Detonation proof foot valve KITO® NRV-...-IIB3 (G 12 N)
Uni-directional end-of-line liquid detonation flame arrester KITO® FL/IN-...-IIB3 (G 14 N)
Gas compensation pipe / venting and breather pipe:
Uni-directional in-line detonation flame arrester, short-time burning proof KITO® FDN-Det4-IIA-…-1,2 (G 18.1 N) with or without Pressure and vacuum relief valve KITO® VD/oG-… (E 21 N)
Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/KS-IIA-…-K (E 13.1 N)

## Slide 10: Protection of external floating roof tanks
Rim venting:
Deflagration and endurance burning proof pressure relief valve KITO® DS/KS-IIA-…-K (C 7 N) alternative Pressure relief valve KITO® DS/o-…(C 8.1 N), not explosion-proof

## Slide 11: Protection rail tank cars and road tanker
Filling pipe:
Uni-directional end-of-line liquid detonation flame arrester KITO® FL/INO-…-IIB3 (G 14.1 N)
Suction pipe:
Detonation proof foot valve
KITO® NRV-...-IIB3 (G 12 N)
Waste gas pipe:
Bi-directional in-line detonation flame arrester, short-time burning proof KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)
Breather and venting pipe: Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/KS-IIA-…-K (E 13.1 N)
Gas compensation pipe: Uni-directional in-line detonation flame arrester, short-time burning proof
KITO® FDN-Det4-IIA-…-1,2 (G 18.1 N)

## Slide 12: Protection rail tank cars and road tanker
Suction and filling pipe:
Uni-directional in-line liquid detonation flame arrester, short-time burning proof KITO® FL/E-...-IIB3 (G 13 N)
Waste gas pipe:
Bi-directional in-line detonation flame arrester, short-time burning proof KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)
Breather and venting pipe:
Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/KS-IIA-…-K (E 13.1 N)
Gas compensation pipe:
Bi-directional in-line detonation flame arrester, short-time burning proof
KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)

## Slide 13: Protection of ship loading stations
Emergency venting and breathing of the ships unloading or loading :
Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/MC-IIA-…-… (E 16.9 N)
Tank venting: Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/MC-IIA-…-… (E 16.9 N)
Emergency venting : Pressure relief valve KITO® EV/o-… (C 10.1.N)
Detonation flame arrester :
Bi-directional in-line detonation flame arrester, short-time burning proof KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)
Deflagration flame arrester : Bi-directional in-line deflagration flame arrester, short-time burning proof KITO® EFA-Def0-IIA-…/…-1,2 (H 35 N)

## Slide 14: Protection of a biogas plant
Bi-directional in-line detonation flame arrester, short-time burning proof KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)
In-line pressure and vacuum relief valve KITO® VD/TG-…(F 31 N)
Deflagration and endurance burning proof ventilation hood KITO® BEH-5-IIA-…-K (B 1 N)
Bi-directional in-line deflagration flame arrester, endurance burning proof KITO® INE-DB-I-…/… (H 32.1 N)
Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/KS-IIA-…-A (E 13 N)

## Slide 15: Protection of a municipal waste water plant
Bi-directional in-line detonation flame arrester, short-time burning proof KITO® EFA-Det4-IIA-…/…-1,2 (G 22 N)
Bi-directional in-line deflagration flame arrester, short-time burning proof KITO® EFA-Def0-I-…/…-1,2 (H 33 N)
Bi-directional in-line deflagration flame arrester, endurance burning proof KITO® INE-DB-I-…/… (H 32.1 N)
Deflagration and endurance burning proof pressure and vacuum relief valve KITO® VD/KS-IIA-…-A (E 13 N)

## Slide 16
Application | Einsatzgebiet |  | Application | Einsatzgebiet
Gas engines | Gasmotoren |  | Filling and emptying lines of container, vessels | Be- und Entleerrungsleitungen Behälter
Diesel engines, working in explosive atmorphere | Dieselmotoren im EX-Bereich |  | Filling and emptying lines for road tank cars and tanker (ship) | Be- und Entladungsleitungen Schiffe, Fahrzeuge
block heat and power plant | BHKW |  | Gas coupling | Gaspendelung
Biogas plant | Biogasanlage |  | Ethanol plant | Ethanolfabriken
Flare | Fackel |  | LNG plant | LNG Industrie
Digester | Faulturm |  | Pressure relief station of gas pipelines | Druckentlastungsstation Gaspipelines
Sewer-gas plant | Klärgasanlage |  | Small mobile tanks | Kleine mobile Tanks
Gas boiler | Gaskessel |  | Protection of the tanks of helicopters | Hubschrauberabsicherung
Biodiesel plant | Biodieselanlage |  | Protection of the tanks of air crafts | Flugzeugabsicherung
Alcohol industrie (distillery, brewery…) | Alkoholindutrie |  | Airport | Flughafen
Industrial adhesive production | Klebstoffherstellung |  | Desulphurisation plant | Gasentschwefelung
Solvent industry | Lösemittelindustrie |  | Gas pumps | Gaspumpen
Lack (paint) industry | Lackindustrie |  | Gas fans | Ventilatoren
Chemical and process industry | Chemie- und Prozessindustrie |  | Gas analyser | Analysegasschränke
Oil and petrolium industrie | Erdöl-, Erdgasindustrie |  | Gas treatment plant | Gasaufbereitungsanlage
Storage tanks / tank farm | Tanklager |  | Sewage treatment plant | Kläranlage

## Slide 17
Application | Einsatzgebiet |  |  | 
Tanker (road, rail) | Tankfahrzeuge (Schiene, Straße) |  |  | 
Mining industry, underground vehicles | Bergbau, Untertagefahrzeuge |  |  | 
Forklift (Ex-Atm.) | Gabelstapler (Ex-Bereich) |  |  | 
Lining of wooden board | Holzbeschichtung |  |  | 
Lining of paper | Papierbeschichtung |  |  | 
Aroma industry | Aromastoffindustrie |  |  | 
Instant coffee plant | Löslicher Kaffee - Herstellung |  |  | 
Glass forming plant (furnace) | Glasschmelze |  |  | 
Flow straightener | Strömungsgleichrichter |  |  | 
Pharmaceutical industry | Pharmazeutische Industrie |  |  | 
Cosmetic industry (e.g. nail polish) | Kosmetische Industrie |  |  | 
Silo protection | Siloabsicherung |  |  | 
Mining industry, gas exhaustion system of bore holes | Bergbau, Gasabsaugung Bohrlöcher |  |  | 

## Slide 18
EFA-Def.
Biogas-flare

## Slide 19
EFA-Def.
Biogas flare

## Slide 20
INE
Biogas flare

## Slide 21
CFA-Def.
Biogas flare
Biogas engine, power supply

## Slide 22
INE
Biogas plant

## Slide 23
EFA-Def.
Biogas plant

## Slide 24
INE
Biogas plant

## Slide 25
INE
Biogas plant

## Slide 26
EFA-Def.
Exhaust gas treatment

## Slide 27
DS/M,
Tank farm

## Slide 28
EV/O Emergency relief
Tank farm

## Slide 29
VD/TG + EFA
Dye- and paint industry

## Slide 30
BEH, electrical heated

## Slide 31
DS/o, old VS/Ka (VS/KS)
Tank farm

## Slide 32
VS/KS
Tank farm

## Slide 33
RG-Det.
Gas analyzer

## Slide 34
RV/N
Degassing system of tank ships

## Slide 35
RV/N,
Waste gas treatment

## Slide 36
Old RV/D2

## Slide 37
VS/cont.
Rail tank car

## Slide 38
VD/o3 + EFA
Chemical industry

## Slide 39
RV/N
Exhaust gas treatment

## Slide 40
Old Rw/Tg + Old DS/Ka,
Refinery

## Slide 41
Old Rd/T

## Slide 42
Old Rd/T + VD/TA-1

## Slide 43
DS/M
Tank farm

## Slide 44
BEH/M, electrical heated
Biogas digester

## Slide 45
VS/KS, electrical heated,
Tank farm

## Slide 47
What kind of devices, which we don´t have, do you need in your market?
Do you have special requirements?
What can we do to support you?
- Problems with KITO®?